ELET3120 (EL31L) – CLASS TEST #1 (18 October 2005)

( 1 )	Calculate the output frequency of the oscillator in Figure 1

and state the type of oscillator.				[3+1]

( 2 )	Replacing the 0.1 μF capacitor in Figure 1 with a 0.01 μF capacitor

results in:							[ 1 ]

( a ) An increase in oscillator frequency.

( b ) A decrease in oscillator frequency.

( c ) Decreased feedback and output waveform distortion.

( d ) Increased feedback and an oscillator that does not work.

( 3 )	What type of oscillator is shown in Figure 2 and calculate the

resonant frequency.						[1 + 3]

( 4 )	An AM waveform has a maximum amplitude of 120 volts

peak- to-peak and a minimum amplitude of 40 volts peak-to-peak.

The percent of modulation is: 				[1]

( a )	33.33%

( b )	50%

( c )	66.67%.

( d )	80%.

( 5 )	A superheterodyne receiver which has an IF of 455 kHz is tuned

to receive a standard AM station that has a frequency of 790 kHz.

Explain what other frequencies reach the IF amp and what station

would cause an 'image' problem. 				[3]

( 6 )	What signals are transmitted by a single-sideband, suppressed- carrier, transmitter when no

modulating signal is present?					[1]

( a ) The upper sideband only

( b ) The lower sideband only

( c ) Both the upper and lower sidebands

( d ) No signal is transmitted

( 7 )	 Calculate the modulation index and the bandwidth when an FM carrier is

deviated 25kHz by a 5kHz modulating signal.

HINT: the highest order sideband (with enough energy to merit consideration)

is the 8th 										[2]

( 8 )	In Phase Modulation, the frequency deviation is proportional to the modulating

signal’s:									 	 [1]

( a ) Amplitude only

( b ) Frequency only

( c ) Amplitude and Frequency

( d ) Phase angle only

( 9 )	 Figure 3 shows the frequency composition of a wave. State what type of wave.	[1]

( 10 )	State the type of modulator shown in Figure 4 then explain the function(s) of the output

section (circuit), after the transistors.		[4]

( 11 )	What is the purpose of a balanced modulator? [1]		[1]

( a ) To eliminate the upper sideband

( b ) To eliminate the lower sideband

( c ) To eliminate the carrier

( d ) To eliminate both sidebands

( 12 )	Draw a labelled, block diagram of a typical AM superhet receiver.		[4]

( 13 )	What class of operation must a transistor be biased for to function as an AM detector?  [1]

( a ) A

( b ) B

( c ) C

( d ) AB

( 14 )	Briefly explain the function of the Beat Frequency Oscillator (BFO).		[3]

( 15 )	A bandpass filter in the IF section of a receiver will: 			[1]

( a ) Improve the sensitivity

( b ) Improve the selectivity

( c ) Improve both selectivity and sensitivity

( d ) Improve image rejection

( 16 )	Briefly mention how can a receiver's images be reduced? 			[2]

( 17 )	A receiver's ability to receive both very weak and extremely strong

stations without introducing distortion is called its: 				[1]

( a ) Sensitivity

( b ) Dynamic range

( c ) Selectivity

( d ) Image rejection

*****   Maximum mark = 35   *****

Bonus mark:	Name the Maker/Manufacturer of the kits used in the Lab.