ELET3120 – Communication Circuits -  Class Test 1 - Friday, March 2, 2012

- Give two reasons why audio is not transmitted at it’s original frequency ?

- What are  three disadvantages of the tuned RF receiver  ?

- What is the bandwidth of an AM signal when the highest modulating

frequency is 10kHz ?

- A 100V. p-p unmodulated carrier has a minimum amplitude of  20V. p-p when modulated , what is the maximum p-p voltage of the modulated waveform and what is the percentage of modulation ?

- What are the three disadvantages of standard AM ?

- Give the most significant advantage and disadvantage of suppressed carrier AM.

- Draw a block diagram (5 blocks) of a superheterodyne receiver.

- List the three characteristics of  Frequency Modulation?

- What is the modulation index when a carrier is deviated 35kHz by a 10kHz signal?

- Give the characteristics of the Absorption Modulator and its typical usage.

12.  What is the power in the upper sideband, for a carrier of 150W. at 75% modulation ?

- With the aid of a diagram show how Frequency Modulation can be obtained from a

Phase Modulator.

14.  What factors must be considered when selecting an Intermediate Frequency  (IF) ?

15.   What is the purpose of a synchronous detector circuit  ?

16.   Define the terms sensitivity and selectivity as used in radio communications ?

- When does maximum deviation occur in a phase modulated wave ?

- When is an AFC circuit required ?

- Which FM detector circuit is suitable for FSK signaling  ?

- What is the image frequency when  a superhet receiver , with an IF of 455kHz,  is tuned to 10.5 MHz.

- What is the primary advantage of an indirect FM modulator ?