# ELET3120 Communications Circuits CLASS TEST 2  Thursday, November 16, 2006

- An FM transmitter is transmitting at 90MHz with plus/minus 54kHz

deviation and this transmitter  uses a frequency doubler and two

frequency triplers between the modulator and the power amplifier.

What is the frequency of the master oscillator

and what is it’s deviation ?							[2]

- Explain the difference between a direct and an indirect FM modulator		[2]

- Name 5 types of FM demodulator circuits, and state which one does

not require a limiter ?								[6]

- Why is 10.7MHz a good choice for the standard IF in FM receivers ? 		[2]

- Draw a block diagram of a phased locked loop (PLL) FM demodulator		[4]

- Is the stereo FM system an example of frequency or time

division multiplexing ?								[1]

- List the advantages and disadvantages of balanced versus unbalanced

transmission line.								            [4]

8.   What determines the characteristic impedance of a transmission line ?		[2]

- If the input impedance of an antenna is 300 ohms and it is fed by a

600 ohm balanced transmission line, what is the SWR on the line ?		[1]

10. What is the impedance of a half-wave dipole antenna ?				[1]

- Draw a diagram to show clearly what is a director and what is a reflector

and indicate on your diagram the effect that these parasitic elements have

on the antenna performance and  explain why these elements

are called parasitic.								[6]

12. Name two examples of a driven array.						[2]

- What is the most significant advantage of a driven array over a parasitic

array ?										[2]

- Name the three types of radio wave propagation and indicate the

frequency band for each type.							[6]

15. What are two causes of fading in radio communications ?			[2]

16.What is the name of the atmospheric layer that is responsible for long

range radio communication and what is the cause of the most significant

variations in this layer.								[2]

17.What two methods can be used to extend the range of VHF, UHF and

higher frequency communications ?						[2]