UNIVERSITY OF THE WEST INDIES

CAVE HILL CAMPUS

Department of Computer Science, Mathematics & Physics

# ELET3120  -  Communication Circuits

# Class Test 2						       Wednesday, March 29, 2017

- What type of multiplexing is used in the stereo FM system ?			[1]

- With the aid of a diagram explain the difference between frequency

inversion and  frequency conversion					            [4]

- What is the impedance of a half-wave dipole antenna ?				[1]

- A piece of balanced transmission line is SHORT CIRCUITED at the end

and is exactly ¼ wavelength at 300 MHz.  Is it series or parallel resonant ?

Will it be series or parallel resonant at 600 MHZ ?  If the short circuit is

removed at	 600 MHz will the line be series or parallel resonant ?		[3]

- What are three methods that can be used to extend radio communication

beyond the horizon ?								[3]

- What is the most significant advantage of a driven array over a parasitic

array ?										[1]

- If the input impedance of an antenna is 300 ohms and it is fed by a

75 ohm unbalanced transmission line, what is the SWR on the line ?		[1]

8. What is the difference between a direct and an indirect FM modulator ?		[2]

9. What are two causes of fading in radio communications ?			[2]

10. List the four parameters that cause variations of the ionosphere			[4]

11. In a direct FM transmitter, what happens to the frequency deviation when:

(a) the amplitude of the modulating signal is increased			[2]

(b) the frequency of the modulating signal is decreased			[2]

12.  Name two example of a driven array						[2]

13. What is the advantage of the shunt-fed Hartley over the series-fed

Hartley.										[2]

14. In the context of commercial television systems, describe the function of:

(a) Diplexer (b) Sync Separator (c) Matrix					[6]