# EL31P  CLASS TEST #2                                            Friday, 11 APRIL 2003

- Perform binary division of 10111001  by 10011                                                  (3)

- Perform modulo 2 division (XOR) of 10011011 by 10110		          	(3)

- When a USB device is first plugged in, which wires get connected first -

signal or power  ?                                                                                                 (1)

4.   Give the SIX Device States defined in the USB specification			(6)

5.   Give the FOUR data Transfer Types defined in the USB specification              (4)

6.    This bit pattern was received in a Hamming system (8 data + 4 parity)

101101001001, correct the error in this bit pattern.			            (5)

- Explain what is "bit checking" as it relates to the CAN protocol		(3)

- Explain what is meant by the terms “pull up” resistor and “pull down”

resistor ?                                                                                                              (2)

9.    Explain what  is "Residual Error Probability"					(3)